## Slide 1: Media Control Profile(MCP) Introduction
Chunhao Jiang, CSPD
Jen, 2024

## Slide 2: Agenda
Concepts
Service & Characteristics
ASE State Management
ASE Characteristics
ASE Control Point Characteristics
ASE State Machine
ASE Test Suite
Notes: 这是说

## Slide 3: Concepts
Media Control Client: initiates playing and pausing, determines playing order, and collects search results from the Media Control Server.
Media Control Server: manage media tracks and conveys the various states and settings to the Media Control Client.
Object Transfer Service: Secondary Service, shall be included from the instance of the MCS or GMCS that it is associated with.

## Slide 4: Media Control Client procedures
Read Media Information procedure
  Discover the media player information on a Media Control Server.
  Read the characteristic value of the Media Player Name characteristic. (Can be set notification)
  When the Media Player Name characteristic is notified, the client should read characteristics such as Media Player Icon Object ID, Media Player Icon URL, and other characteristics that could have changed because of the Media Player Name change.
Read Media Player Icon Object Information procedure
  discover the media player icon as an object in the included Object Transfer Service

## Slide 5: Media Control Client procedures
Procedure | function | Propority | Notes
Read Media Information | Discover the media player information | Read | Read the characteristic value of the Media Player Name characteristic can be set notification.
Read Media Player Icon Object Information | discover the media player icon as an object | Read | 
Read Track Title | Discover the current track information | Read/Notify | 
Read Track Duration | discover the current track duration | Read | 
Read Track Position | discover the current track position | Read/Notify | Track Position characteristic is not notified to the client when the Track Position is changing because of playing the track.
Set Absolute Track Position | set the current track position on a Media Control Server to an absolute position. | Write | 
Set Relative Track Position | set the current track position on a Media Control Server to a position relative to the current track position. | Write/Notify | using the Move Relative opcode and the parameter set to the relative time of the move.

## Slide 6: Media Control Client procedures
Procedure | function | Propority | Notes
Read Playback Speed | discover the current playback speed of the current track | Read | 
Set Playback Speed | set the playback speed of the current track | Write | 
Read Seeking Speed | discover the current track seeking speed | Read | 

## Slide 7: Media Control Client procedures
Procedure | function | Propority | Notes
Read Media Information | Discover the media player information | Read | Read the characteristic value of the Media Player Name characteristic can be set notification.
Read Media Player Icon Object Information | discover the media player icon as an object | Read | 
Read Track Title | Discover the current track information | Read/Notify | 
Read Track Duration | discover the current track duration | Read | 
Read Track Position | discover the current track position | Read/Notify | Track Position characteristic is not notified to the client when the Track Position is changing because of playing the track.

## Slide 8: Media Control Client procedures
Procedure | function | Propority | Notes
Read Media Information | Discover the media player information | Read | Read the characteristic value of the Media Player Name characteristic can be set notification.
Read Media Player Icon Object Information | discover the media player icon as an object | Read | 
Read Track Title | Discover the current track information | Read/Notify | 
Read Track Duration | discover the current track duration | Read | 
Read Track Position | discover the current track position | Read/Notify | Track Position characteristic is not notified to the client when the Track Position is changing because of playing the track.

## Slide 9: Media Control Client procedures
Read Track Title procedure
  Discover the current track information on a Media Control Server.
  Read the characteristic value of the Track Title characteristic. (Can be set notification).
Read Media Player Icon Object Information procedure
  discover the media player icon as an object in the included Object Transfer Service

## Slide 10: Service & Characteristics
Service
  There shall be no more than one ASCS instance on a server.
  ASCS shall be a Primary Service and the service UUID shall be set to Audio Stream Control
  ASCS can be instantiated on devices that can accept the establishment of unicast Audio Streams

## Slide 11: Service & Characteristics
Characteristics
  Sink ASE Characteristic: The server is said to act as Audio Sink for that ASE. There can be more than one Sink ASE characteristic on the server.
  Source ASE Characteristic: The server is said to act as Audio Source for that ASE. There can be more than one Source ASE characteristic on the server.
  ASE Control Point Characteristic: An ASE Control Point characteristic that clients use to configure parameters for each ASE exposed by the server. The ASE Control Point characteristic is used to operate on all ASEs, distinguishing each ASE by its ASE_ID value. Only one instance exist on the server.

## Slide 12: ASE State Management
Maintained by the server and shared with a
client using ASE characteristics.
State(ASE_state) & Operation(opcode)
Client can control state machine by writing to
the ASE Control Point characteristics
Server can autonomously control state machine
Client can read current state of server
Server can notify client current state
Sink ASE
Source ASE

## Slide 13: ASE Characteristics
Same characteristic have same UUID,
but have different handle, handle
indicate different stream, ASE_ID is unique in same client and in same UUID.
Client ASE reading or being notified ASE characteristic value cannot gain any information about the ASE characteristic value at the same attribute handle that is exposed for a different client.
The server should allocate local resources which can be affected by a change in the state of an ASE as it sees fit. The behavior of the server in deciding whether to accept client requests that can change the state of an ASE is left to the implementation.
If the characteristic value changed:
  If connecting and notification is configured, then notify immediately
  If not connecting but bonded, but notification is configured, then notify when reconnect

## Slide 14: ASE Control Point Characteristics
The opcode is used by the server to determine which ASE Control operation is being initiated by the client.
A notification of the ASE Control Point is used to provide a response to a client-initiated ASE Control operation.

## Slide 15: ASE State Machine
ASE Control operations can be initiated by server or client.
Initiated by client
  Success: send a notification of ASE Control Point to client.
  Can execute all of the operations except Released operation,
  and send ASE values during that ASE Control operation.
  Fail: send a notification to client with reason and additional
  information.
Initiated by server
  Can execute all of the operations, and send ASE values during
  that ASE Control operation. Not send a notification of the ASE
  Control Point characteristic value when completing an
  autonomously-initiated ASE Control operation.
All of the parameters have Number_of_ASEs and ASE_ID[i]
Sink ASE
Source ASE

## Slide 16: ASE State Machine
Codec Configurate
  Target latency: expect server return meaningful
  values for QoS preferences:
    low latency, balance, high reliability.
  Target PHY: 1M/2M/Coded
  Codec ID: Coding format, Company ID, VS codec ID
  Codec Specific Configuration
Sink ASE
Source ASE

## Slide 17: ASE State Machine
QoS Configurate
  The Config QoS operation is used to request a CIS
  configuration preference with the server and to
  assign identifiers to the CIS.
  CIS can exist except Idle and Codec Configures,
  because CIS parameters can be configured when
  QoS configured
  The server shall not accept the Config QoS operation
  for that ASE if the configuration result in more than
  one Sink/Source ASE having identical CIG_ID and
  CIS_ID parameter values for that client
  Parameters: CIS ID, CIG ID, SDU Inertval, Max SDU,
  Retransmission Number, Max Transport Latency,
  Presentation Delay
Sink ASE
Source ASE

## Slide 18: ASE State Machine
Enable
  Request the server to enable an ASE and to
  provide any Metadata applicable for that ASE.
  Start coupling ASE to a CIS.
  If a CIS has been established and the server is
  acting as Audio Sink for the ASE, and if the server
  is ready to receive audio data transmitted by the
  client, the server may autonomously initiate the
  Receiver Start Ready, without first sending a
  notification of the ASE characteristic value in the
  Enabling state.
Sink ASE
Source ASE

## Slide 19: ASE State Machine
Receiver Start Ready
  Sink -> Source
    Inform Source that the Sink is ready to consume audio data
    transmitted by the Source.
Disable
  Request the server to disable an ASE
  Decouple CIS.
Disabling
  Ensures consistent delivery and coordination of audio
  streams.
Receiver Stop Ready operation
  Client(Sink) inform a server (Source) that the client is ready to stop
  consuming audio data transmitted by the server.
Sink ASE
Source ASE

## Slide 20: ASE State Machine
Release
  Request the server to release an ASE and all resources
  associated with that ASE.
Released
  Initiated autonomously by the server if:
    The server has detected the loss of the LE-ACL for
    an ASE in any state, or
    Release have completed, and the server controller
    has indicated that CIS has been torn down
  Server can choose to cache a codec configuration
  or not cache codec configuration
Sink ASE
Source ASE

## Slide 21: ASE Test Suite
Generic GATT Integrated Tests
Additional Service Requirements
  Server IUT supports a single instance of the Audio Stream Control Service and follows the requirements for the supported characteristics of the service when multiple ASEs are present.
    Lower Tester executes the GATT Read Characteristic Value sub-procedure.
ASE Control Point Procedures
  Different roles transfer to different status performance from different valid status.
    The Lower Tester writes to the ASE Control Point and get the notification from server.
  Server Initiates Released Operation from dropped LE-ACL
    Lower Tester tears down connection and IUT start extended adv, Lower Tester reconnect and read characteristics by executing the GATT Read Characteristic (should be Idle or Codec Configured)

## Slide 22: ASE Test Suite
Service Procedure – Error Handling
  Invalid Opcode
    Set a RFU value of opcode
  Common Control Point errors
    Set invalid ASE identifiers and Control Point commands of invalid length
  Invalid ASE_ID Errors
  Invalid Parameters for different operations
  Invalid State Transition
  Config QoS with Different ASE with Same Direction, CIG, and CIS

## Slide 23
Thank you for listening!