## Slide 1: Audio Stream Control Service (ASCS) Introduction
Chunhao Jiang, CSPD
Nov, 2023

## Slide 2: Agenda
Concepts
Service & Characteristics
ASE State Management
ASE Characteristics
ASE Control Point Characteristics
ASE State Machine
ASE Test Suite
Notes: 这是说

## Slide 3: Concepts
Audio Sink: Receives unicast audio data from Audio Sources
Audio Source: Transmits unicast audio data to Audio Sinks
Audio Stream Endpoint (ASE): The endpoint of a unicast Audio Stream, which audio data flows to or from; exists on the server.
GATT Server & Client
GATT read & write & notify

## Slide 4: Service & Characteristics
Service
  There shall be no more than one ASCS instance on a server.
  ASCS shall be a Primary Service and the service UUID shall be set to Audio Stream Control
  ASCS can be instantiated on devices that can accept the establishment of unicast Audio Streams

## Slide 5: Service & Characteristics
Characteristics
  Sink ASE Characteristic: The server is said to act as Audio Sink for that ASE. There can be more than one Sink ASE characteristic on the server.
  Source ASE Characteristic: The server is said to act as Audio Source for that ASE. There can be more than one Source ASE characteristic on the server.
  ASE Control Point Characteristic: An ASE Control Point characteristic that clients use to configure parameters for each ASE exposed by the server. The ASE Control Point characteristic is used to operate on all ASEs, distinguishing each ASE by its ASE_ID value. Only one instance exist on the server.

## Slide 6: ASE State Management
Maintained by the server and shared with a
client using ASE characteristics.
State(ASE_state) & Operation(opcode)
Client can control state machine by writing to
the ASE Control Point characteristics
Server can autonomously control state machine
Client can read current state of server
Server can notify client current state
Sink ASE
Source ASE

## Slide 7: ASE Characteristics
Same characteristic have same UUID,
but have different handle, handle
indicate different stream, ASE_ID is unique in same client and in same UUID.
Client ASE reading or being notified ASE characteristic value cannot gain any information about the ASE characteristic value at the same attribute handle that is exposed for a different client.
The server should allocate local resources which can be affected by a change in the state of an ASE as it sees fit. The behavior of the server in deciding whether to accept client requests that can change the state of an ASE is left to the implementation.
If the characteristic value changed:
  If connecting and notification is configured, then notify immediately
  If not connecting but bonded, but notification is configured, then notify when reconnect

## Slide 8: ASE Control Point Characteristics
The opcode is used by the server to determine which ASE Control operation is being initiated by the client.
A notification of the ASE Control Point is used to provide a response to a client-initiated ASE Control operation.

## Slide 9: ASE State Machine
ASE Control operations can be initiated by server or client.
Initiated by client
  Success: send a notification of ASE Control Point to client.
  Can execute all of the operations except Released operation,
  and send ASE values during that ASE Control operation.
  Fail: send a notification to client with reason and additional
  information.
Initiated by server
  Can execute all of the operations, and send ASE values during
  that ASE Control operation. Not send a notification of the ASE
  Control Point characteristic value when completing an
  autonomously-initiated ASE Control operation.
All of the parameters have Number_of_ASEs and ASE_ID[i]
Sink ASE
Source ASE

## Slide 10: ASE State Machine
Codec Configurate
  Target latency: expect server return meaningful
  values for QoS preferences:
    low latency, balance, high reliability.
  Target PHY: 1M/2M/Coded
  Codec ID: Coding format, Company ID, VS codec ID
  Codec Specific Configuration
Sink ASE
Source ASE

## Slide 11: ASE State Machine
QoS Configurate
  The Config QoS operation is used to request a CIS
  configuration preference with the server and to
  assign identifiers to the CIS.
  CIS can exist except Idle and Codec Configures,
  because CIS parameters can be configured when
  QoS configured
  The server shall not accept the Config QoS operation
  for that ASE if the configuration result in more than
  one Sink/Source ASE having identical CIG_ID and
  CIS_ID parameter values for that client
  Parameters: CIS ID, CIG ID, SDU Inertval, Max SDU,
  Retransmission Number, Max Transport Latency,
  Presentation Delay
Sink ASE
Source ASE

## Slide 12: ASE State Machine
Enable
  Request the server to enable an ASE and to
  provide any Metadata applicable for that ASE.
  Start coupling ASE to a CIS.
  If a CIS has been established and the server is
  acting as Audio Sink for the ASE, and if the server
  is ready to receive audio data transmitted by the
  client, the server may autonomously initiate the
  Receiver Start Ready, without first sending a
  notification of the ASE characteristic value in the
  Enabling state.
Sink ASE
Source ASE

## Slide 13: ASE State Machine
Receiver Start Ready
  Sink -> Source
    Inform Source that the Sink is ready to consume audio data
    transmitted by the Source.
Disable
  Request the server to disable an ASE
  Decouple CIS.
Disabling
  Ensures consistent delivery and coordination of audio
  streams.
Receiver Stop Ready operation
  Client(Sink) inform a server (Source) that the client is ready to stop
  consuming audio data transmitted by the server.
Sink ASE
Source ASE

## Slide 14: ASE State Machine
Release
  Request the server to release an ASE and all resources
  associated with that ASE.
Released
  Initiated autonomously by the server if:
    The server has detected the loss of the LE-ACL for
    an ASE in any state, or
    Release have completed, and the server controller
    has indicated that CIS has been torn down
  Server can choose to cache a codec configuration
  or not cache codec configuration
Sink ASE
Source ASE

## Slide 15: ASE Test Suite
Generic GATT Integrated Tests
Additional Service Requirements
  Server IUT supports a single instance of the Audio Stream Control Service and follows the requirements for the supported characteristics of the service when multiple ASEs are present.
    Lower Tester executes the GATT Read Characteristic Value sub-procedure.
ASE Control Point Procedures
  Different roles transfer to different status performance from different valid status.
    The Lower Tester writes to the ASE Control Point and get the notification from server.
  Server Initiates Released Operation from dropped LE-ACL
    Lower Tester tears down connection and IUT start extended adv, Lower Tester reconnect and read characteristics by executing the GATT Read Characteristic (should be Idle or Codec Configured)

## Slide 16: ASE Test Suite
Service Procedure – Error Handling
  Invalid Opcode
    Set a RFU value of opcode
  Common Control Point errors
    Set invalid ASE identifiers and Control Point commands of invalid length
  Invalid ASE_ID Errors
  Invalid Parameters for different operations
  Invalid State Transition
  Config QoS with Different ASE with Same Direction, CIG, and CIS

## Slide 17
Thank you for listening!